DEV   7231/7331

Optribution Basic l-band link

Empfohlen für „RF-over-Fiber“-Links mit optischen Verlusten bis 10 dB

Fixe Verstärkung

HF-Signalerkennung mit Status LED

LNB Power mit Stromüberwachung und Status LED

Optischer Stecker-Typ SC/APC (optional FC/APC oder E2000 HRL)

spezifikationen

| dev 7231 & Dev 7331 | value | condition |
| --- | --- | --- |
| Frequency Range | 950…2150 MHz |  |
| Max. Link Gain | 4±3 dB |  |
| Flatness | ±1.5 dB ±0.2 dB | 950…2150 MHz In any 36 MHz window |
| Return Loss | >14 dB, typ. 16 dB |  |
| Gain Stability | ±2 dB | 0...+50 °C / 32…122 °F |
| Group Delay Distortion | <2 ns |  |
| Nominal RF Input Level | -10 dBm | Total power |
| Noise Figure | 24 dB |  |
| SFDR2/3 | 107 dBc | Note 1 |
| CNR | 59 dB | Notes 2, 3, 4 |
| Output IP3 | 16 dBm |  |
| OP1dB | -1 dBm |  |
| Intermodulation Distortion | >40 dBc | @ 2 tones, -13 dBm each |
| Input Power dynamic Range | -45…-6 dBm | Total power |
| Damage RF Input Level | 12 dBm | Total power |
| Maximum allowable optical Losses | 23 dB |  |

Note 1: Pin = -15 dBm, IM3 = 48 dBc

Note 2: Pin = -15 dBm

Note 3: 36 MHz window

Note 4: with back to back fiber connection (2 m) and minimum noise figure

technische daten dev 7231 & dev 7331

| Common Optical Specifications | value | condition |
| --- | --- | --- |
| Fiber Type | Single Mode 9/125 μm |  |
| Optical Connector | SC/APC, E2000/HRL, or FC/APC | Standard is SC/APC |
| Tx Specifications (DEV 7231) |  |  |
| Laser Type | DFB |  |
| Laser Class (according to IEC 60 825-1) | Class 1M (low Risk to Eyes, no Risk to Skin) |  |
| Optical Power Output | 1 mW / 0 dBm |  |
| Power Consumption | 15 V; 200 mA | Without LNB power |
| Weight | ~0.5 kg |  |

| Tx LNB Power & Current Monitoring |  |  |
| --- | --- | --- |
| LNB Power | 18+0/-3 V; max. 500 mA |  |
| Alarm Indication | Via LED on the Front Panel & via Remote Communication |  |
| Rx Specifications (DEV 7331) |  |  |
| Wavelength Range | 1100…1650 nm |  |
| Min. optical Input Level (optical Sensitivity) | -22 dBm |  |
| Damage optical Input Level | +10 dBm |  |
| Power Consumption | 15 V; 200 mA |  |
| Weight | ~0.3 kg |  |
| Tx & Rx RF Sensing |  |  |
| Adjustable Threshold Level (THL) | 0 dBm > THL > -50 dBm (Factory Setting: -30 dBm ) |  |
| Threshold Level Accuracy | ±3 dB |  |
| Threshold Repeatability | <0.5 dB |  |
| Alarm Indication | Via LED on the Front Panel & via Remote Communication |  |
| Tx & Rx General Specification |  |  |
| Size | 4 HP (20 mm) Width, 3 RU (133 mm) Height, 3.94" (100 mm) Depth |  |
| Environmental Conditions | ETS 300019 Part 1-3 Class 3.1 |  |

Bestellinformationen

| PRODUCT |
| --- |
| DEV 7231 | Basic OptributionTransmitter; 950…2150 MHz; SC/APC |
| DEV 7331 | Basic Optribution Receiver; 950…2150 MHz; SC/APC |
| Optical Connector Options |
| Option 07 | FC/APC Optical Connector |
| Option 08 | E2000/HRL Optical Connector |